## Slide 1: Collision Prediction Based On Semantic Relations
30220 - Master Thesis Presentation
Rakesh Allampally, Chemnitz, February 2021

## Slide 2: Contents:
SUMO
Semantic Entity Relational (Approach-1)
Goals
Basic Overview of Approach
Recurrent Neural Networks
Long Short Term Memory Network (LSTM)
1) Recursive Forecast & Results
2) Encoder-Decoder & Results
Entity Relation for Single Vehicle (Approach-2)
Collision Test Scenarios & Results
Conclusion & Future Work

## Slide 3: SUMO
Highway Scenario in SUMO
IAV 12/2020 IAV TI-F21

## Slide 4: Semantic Entity Relation (Approach-1)
At each time step we get the information of all the objects in the scene and their relations
Relational Grid Model [1]
[1] https://www.groundai.com/project/adaptive-behavior-generation-for-autonomous-driving-using-deep-reinforcement-learning-with-compact-semantic-states/1
IAV 12/2020 IAV TI-F21

## Slide 5: Goals
Use semantic entity relationship model to get complete overview of the scene.
Use RNN to predict trajectory of all the vehicles in the scene by using the past trajectory.
Finally, developed model test on various collision probable scenarios.
IAV 12/2020 IAV TI-F21

## Slide 6: Basic Overview of Approach
For each time stamp, the Ego vehicle and its surroundings are considered.
The surroundings are in the range of 50 meters.
ID of the Ego vehicle is fixed but remaining vehicles IDs keeps changing.
Rel. P, V, A = Relative position, velocity, acceleration with respect to Ego.
IAV 12/2020 IAV TI-F21
Relational Grid Model

## Slide 7: Recurrent Neural Networks
The output from the previous step is fed as input to the current step along with the current Input.
It has a hidden state, which remembers the information about a sequence.
Hidden state at time ‘t’,
= Input at time ‘t‘
IAV 12/2020 IAV TI-F21
Recurrent Neural Networks [2]
[2] https://colah.github.io/posts/2015-08-Understanding-LSTMs/

## Slide 8: Problem with RNN
The main problem of RNN is long term dependency.
IAV 12/2020 IAV TI-F21
[2] https://colah.github.io/posts/2015-08-Understanding-LSTMs/
Less Time Steps [2]
More Time Steps [2]

## Slide 9: Long Short Term Memory Network (LSTM)
In LSTM both cell state are passed to the next time step.
Cell state acts as memory of the network and carries relevant information throughout processing
of the sequence.
In LSTM the the 3 gates namely Input gate, Forget gate, Ouptut gate decide which information is allowed on the cell state.
IAV 12/2020 IAV TI-F21
[2] https://colah.github.io/posts/2015-08-Understanding-LSTMs/
LSTM [2]

## Slide 10: Long Short Term Memory Network (LSTM)
Forget Gate
IAV 12/2020 IAV TI-F21
Input Gate

## Slide 11: Long Short Term Memory Network (LSTM)
Updated Cell State
IAV 12/2020 IAV TI-F21
Output Gate

## Slide 12: Time Series Data:
Input data: t-39, t-39, t-38, ………., t-1, t [40 time-steps]
For current models we get only single step prediction ahead.
Predicted data : t+1 [1 time-step]
Multi-step prediction:
To predict more than one step ahead, we should use multistep prediction.
Some of the multi-step prediction models are:
1) Recursive Forecast
2) Encoder-Decoder
IAV 12/2020 IAV TI-F21

## Slide 13: 1) Recursive Forecast (Approach-1)
Input data: t-39, t-39, t-38, ………., t-1, t [40 time-steps]
Predicted data : t+1 [1 time-step]
First iteration:
Input: t-38, ………., t-1, t, t+1 [40 time-steps]
Predicted data : t+2 [1 time-step]
Second iteration:
Input: t-37, ………., t-1, t, t+1, t+2 [40 time-steps]
Predicted data : t+3 [1 time-step]
Repeat these for 20 iterations
Predicted data : t+1, t+2, t+3, ………., t+20 [20 time-step]
IAV 12/2020 IAV TI-F21
[3] A. Sorjamaa and A. Lendasse, “Time series prediction using dirrec strategy.,”inEsann, vol. 6, pp. 143–148, 2006.
Recursive Forecast [3]

## Slide 14: Recursive Forecast
Number of lstm layers = 2
Number of neurons = 56
Number of epochs = 50
Time taken for each epoch = 32 seconds
Trained scenes - 50
Tested scenes - 15
IAV 12/2020 IAV TI-F21
Training loss vs Validation loss

## Slide 15: Prediction Result of Right-leader
IAV 12/2020 IAV TI-F21
The longitudinal mean absolute error, e = 1.95 meters.
The lateral mean absolute error, e = 0.45 meters.
Longitudinal Position Prediction
Lateral Position Prediction

## Slide 16: 2) Encoder-Decoder (Approach-1)
Input data:
Predicted data :
cell state :‘
is the final cell state vector of the Encoder,
which holds summary of input vector
IAV 12/2020 IAV TI-F21
[4] https://www.semanticscholar.org/paper/Sequence-to-Sequence-Prediction-of-Vehicle-via-LSTM-Park-Kim/528f6933d246ff9d0918f2e936d7bfa79aa7fea9
Encoder-Decoder LSTM [4]

## Slide 17: Encoder-Decoder
Number of LSTM Encoder-Decoder layer = 1
Number of neurons = 256
Number of epochs = 50
Time taken for each epoch = 120 seconds
Trained scenes - 50
Tested scenes - 15
IAV 12/2020 IAV TI-F21
Training loss vs Validation loss

## Slide 18: Prediction Result of Right-leader
IAV 12/2020 IAV TI-F21
The longitudinal mean absolute error, e = 1.4 meters.
The lateral mean absolute error, e = 0.3 meters.
Longitudinal Position Prediction
Lateral Position Prediction

## Slide 19: Entity Relation for Single Vehicle (Approach-2)
IAV 12/2020 IAV TI-F21
Approach-2 Overview

## Slide 20: Encoder-Decoder
Number of LSTM Encoder-Decoder layer = 1
Number of neurons = 512
Number of epochs = 50
Time taken for each epoch = 50 seconds
Trained scenes - 50
Tested scenes - 15
IAV 12/2020 IAV TI-F21
Training loss vs Validation loss

## Slide 21: Prediction Result of Ego-front
IAV 12/2020 IAV TI-F21
The longitudinal mean absolute error, e = 1.6 meters.
Longitudinal Position Prediction

## Slide 22: Test Scene 1
IAV 12/2020 IAV TI-F21
Ego-front collision
Threshold = 2 meters (longitudnal)
Threshold = 1 meter (lateral)

## Slide 23: Test Scene 2
IAV 12/2020 IAV TI-F21
Right-leader collision

## Slide 24: Test Scene 3
IAV 12/2020 IAV TI-F21
Left-leader collision

## Slide 25: Test Scene 4
IAV 12/2020 IAV TI-F21
Right-leader & Left-follower collision

## Slide 26: Test Scene 5
IAV 12/2020 IAV TI-F21
Right-neighbour & Ego-front collision

## Slide 27: Conclusion & Future Work
The mean absolute error is minimal for semantic entity relationship’s based encoder-decoder model.
This can be deployed in real-world autonomous driving cars, by predicting the collision in advance can help to minimize the accidents.
IAV 12/2020 IAV TI-F21

## Slide 28
Rakesh Allampally (TIF 21)
IAV GmbH
Kauffahrtei 25, 09120 Chemnitz Telefon 015258540248
www.iav.com